## Slide 1
Shut the box game is a simple pencil box. It has a string of wooden tiles on a piece of coat hangar wire. (Drilling al the holes in the bottom of the tiles is the hard part.). The wire is inserted in holes in the ends of the box. Find someone in your pack that is handy with woodworking. They can make all ( or most) of the parts so Cubs can assemble. It is important to pre-drill the side nail holes. That will make it easy for cubs make the finish nails look good. For ease of construction, an adult can drill a hole as the cub hammers each nail in the bottom. This will make it much easier for them to drive the nails and keep them straight.
Parts:
2 sides A
1 end piece B
1 end piece C
1 bottom D
1 lid E
9 tiles F

## Slide 2
.
.
.
.
9 3/4”
2”
.
3”
1 3/8”
2”
.
2 of these (sides A)
3”
.
Front
Side
5/16”
3/4”
2 1/2”
9 tiles (F)
Hole part way through to hold the coat hanger wire
Hole Big enough for wire
Here are the plans for a “Shut the Box” game. The one you make doesn’t have to be exactly the same. You just want a pencil box with a string of tiles strung on a coat hangar wire.
2”
3/4”
1 3/8”
Dado slot slightly wider than 1/8”, ¼” deep. Needs to be wide enough for lid E to slide into.
Side view
End View
Pre-drill nail holes
A
B
C
4 ½” x 9 ¾”, 1/8” thin plywood
“Door Skin”
3 3/8”x 9”, 1/8” thin plywood
“Door Skin”
D
E

## Slide 3
.
.
.
Front
Side
9 tiles (F)
B
C
A Note on Hole Placement
The distance from the hole to the bottom and side edge of pieces C and B must be a little larger than the distance from the hole and the bottom edge of the tile. This will allow the tile to rotate unimpeded on the coat hanger wire.
A little larger
A Little Smaller

## Slide 4
Assembly
1. Starting from the side opposite the dado groove in a part A, start 2 finishing nails in two pre-drilled holes at one end.
2. Finish driving the nails into part B. Notice the relative positon of the hole and the groove.
A-1
Top View
End View
A-1
A-1
B
A-1
B
.
3. Starting from the side opposite the dado groove in the other part A, start 2 finishing nails in two pre-drilled holes at one end.
A-2
Top View
End View
A-1
B
A-1
B
.
A-2
A-2
4. Finish driving the nails into part B forming a “U”
Top View
End View
A-2
5. Insert end C to get the spacing, but don’t nail it into place. Place bottom D on “U” and nail with headed nails
A-1
B
.
A-2
.
.
.
.
.
.
.
C

## Slide 5
A-1
C
A-2
A-2
B
A-1
1
2
3
4
5
6
7
8
9
5. With the cub using their best handwriting, put the numbers 1 through 9 on the tiles.
6. String the tiles on the coat hangar wire in numerical order.
1
2
3
4
5
6
7
8
9
7. Turn the tile set so the numbers are face down. Slide into the box and insert the coat hangar wire into the hole in end B.
A-2
B
A-1
C
8. Slide end piece C into place, making sure the coat hangar wire goes into its hole
Top View
End View
9. Nail four finishing nails through the sides into end C.
A-2
B
A-1
C